## Slide 1
Adder Architecture Comparisons
Using Verilog Simulation
Joseph Latocha
ECE 465
Digital Systems Design
Fall 2023

## Slide 2: Motivation
Digital system addition is a fundamental function of most computing systems.
Many different kinds of adder architectures make it an interesting topic of investigation.
  Every architecture has its pros and cons.
Develop a deeper understanding of coding in Verilog, and investigate the trade-offs in each of the adder architectures.
  At the beginning of the semester, I had very little understanding of Verilog, and I wanted to know how I could use Verilog for testing my own future designs to continue my own designs and test these designs on an FPGA.

## Slide 3: Problem Statement
Goals:
  To investigate a variety of adder architectures using Verilog and detail their real-world implementation strengths and weaknesses.
    Ripple-Carry Adder,
    Carry-Lookahead Adder,
    Parallel Prefix,
    Kogge-Stone
  Observe propagation behavior with active clock.
  Investigate architectures’ simulation times (clock-cycles) and complexity.
  Ensure adder correct calculation operation for each adder architecture.

## Slide 4: Techniques – Ripple Carry
Carry bit is propagated bit-by-bit through the daisy-chained full adder structure,
  From least significant bit (LSB) to most significant bit (MSB)
Calculation is done when the appropriate number of clock-cycles has passed
  This is linearly proportional to the number of bits in the ripple-carry adder structure
    E.g. 4-bit ripple-carry achieved in 4 clock cycles, 16-bit ripple-carry calculation is accomplished in 16 clock cycles, and N-bit ripple-carry calculation is accomplished in N clock cycles.
[1]
  Expected time delay of Ripple-Carry adder
Figure 2: 32-Bit Ripple-Carry Block Diagram [1]
Figure 1: 1-Bit Full Adder Circuit [2]

## Slide 5: Techniques – Carry Look-Ahead
Use of generate and propagate signals completes the carry from an addition bit in parallel to summation process.
  P
Propagation delay is significantly reduced compared to ripple-carry
[1]
  Expected time delay of Carry-Lookahead adder
Figure 3: a)32-Bit Carry-Lookahead Block Diagram
b) Enlarged Image of 4-bit CLA Block [1]

## Slide 6: Techniques – Parallel Prefix (Sklansky)
Use of generate and propagate signals completes the carry from an addition bit in parallel to summation process.
Propagation delay is reduced compared to carry-lookahead by computing generate and propagate signals in more of a tree-structure than Carry-Lookahead
[1]
  Expected time delay of Parallel Prefix adder
Figure 4: 16-Bit Parallel Prefix Adder, Red lines denote critical path [1]
Figure 5: 16-Bit Parallel Prefix Adder Legend [1]

## Slide 7: Techniques – Parallel Prefix (Kogge-Stone)
Use of generate and propagate signals completes the carry from an addition bit in parallel to summation process.
Propagation delay is reduced compared to carry-lookahead by computing generate and propagate signals in more of a tree-structure than Carry-Lookahead
Critical path for computation is lessened by more
[1]
  Expected time delay of Kogge-Stone adder
Figure 6: 16-Bit Kogge-Stone Adder, red is critical path [3]

## Slide 8: Results – Ripple Carry
Figure 7: Ripple Carry Adder GTK Waveforms
Test Cases
  32’b 01+32’b 01
    Final result occurs in 1-clock cycle
  32’b 0110+ 32’b 01
    Final result occurs after 1-clock cycle
  32’b 0111+ 32’b 01
    Final result obtained after 4-clock cycles
  32’b 1+ 32’h FFFFFFFF(worst-case)
    Final result obtained after 32-clock cycles

## Slide 9: Results – Ripple Carry – Worst Case

## Slide 10: Results – Ripple Carry – Worst Case

## Slide 11: Results - CLA
Figure 8: Carry-Look Ahead Adder GTK Waveforms
Test Cases
  32’b 01+32’b 01
    Final result occurs in 1-clock cycle
  32’b 0110+ 32’b 01
    Final result occurs after 1-clock cycle
  32’b 0111+ 32’b 01
    Final result obtained after 1-clock cycles
  32’b 1+ 32’h FFFFFFFF(worst-case)
    Final result obtained after 1-clock cycles

## Slide 12: Results – CLA – Terminal Print Out

## Slide 13: Results – Parallel Prefix
Figure 9: GTK Wave Output for Parallel Prefix
Test Cases
  16’b 01+16’b 01
    Final result occurs in 1-clock cycle
  16’b 0110+ 16’b 01
    Final result occurs after 1-clock cycle
  16’b 0111+ 16’b 01
    Final result obtained after 1-clock cycles
  16’b 1+ 16’h FFFF(worst-case)
    Final result obtained after 1-clock cycles

## Slide 14: Results – Parallel Prefix – Terminal Print Out

## Slide 15: Results - Combined
Adder Topology | Simulation Time (clock cycles) | Hardware Cost (number of gates) | Complexity (coding cost)
Ripple-Carry (32-bit) | 32 | 160 gates | LOW
Carry Look Ahead (32-bit) | 1 | 192 gates | MEDIUM
Parallel Prefix (16-bit) | 1 | 162 gates | HIGH
Table 1: Adder Topologies and Their Simulation Time, Hardware Cost, Coding Difficulty
Full Adder hardware cost = =160 gates
CLA hardware cost = = 192 gates
  Sum Gen Prop Carry
PP (Sklansky 16-bit) hardware cost = = 162 gates
PP (Sklansky 32-bit) hardware cost = = 370 gates
  Note: All hardware costs displayed represent 2-input gates

## Slide 16: Deviation From Expected Results
Adder Topology | Simulation Time (clock cycles) | Hardware Cost (number of gates) | Complexity (coding cost)
Ripple-Carry (32-bit) | 32 | 160 gates | LOW
Carry Look Ahead (32-bit) | 1 | 192 gates | MEDIUM
Parallel Prefix (16-bit) | 1 | 162 gates | HIGH
Table 1: Adder Topologies and Their Simulation Time, Hardware Cost, Coding Difficulty
Expected the CLA adder to reach its final result after 4 clock-cycles, but the result was obtained in one.
  This means the CLA may have been inadvertently created with 1-bit ripple carry blocks.

## Slide 17: Conclusion
Ripple-Carry
  Slowest Adder in terms of simulation time (clock-cycles)
  Lowest Hardware cost
  Very easy to code
Carry-Lookahead
  Tied for simulation time (clock-cycles), but propagation delay should be investigated more thoroughly to determine actual simulation time
  Implementation in Verilog was harder than the Ripple-Carry, but easier than the parallel prefix (Sklansky)
Parallel-Prefix
  Tied for simulation time (clock cycles) with CLA
  Most difficult to implement in Verilog

## Slide 18: References
[1] D. M. Harris and S. L. Harris, Digital Design and Computer Architecture, 2nd ed. San Francisco, CA, USA: Morgan Kaufmann, 2012. [2] “Full Adder Circuit,” Implement Logic, Aug. 16, 2011. [Online]. Available: https://implement-logic.blogspot.com/2011/08/full-adder-circuit_16.html.
[3] D. Harris, “A taxonomy of parallel prefix networks,” in Proc. IEEE Symposium on Computer Arithmetic, 2003.